## Slide 1: Engineering Analysis Presentation
The Ångströnomers
Economic Device to measure In-Plane Thermal Conductivity

## Slide 2
Thermal Conductivity: The degree to which thermal energy is transported across a temperature gradient
Q = heat transferred
d = distance between two isothermal regions
A = area
ΔT = change in temperature
Critical for work in Thermal Management
Low-profile electronics require in-plane solutions
  Requires characterization of novel, anisotropic materials
Thermal Conductivity
Notes: Thermal Conductivity: The degree to which thermal energy is transported across a temperature gradient
Through-plane: travels through a material
  Most current test methods are through-plane
In-plane: travels laterally across material
  Companies are trying to move heat laterally, need new materials for thermal management solutions
  In-plane thermal conductivity is key, especially in novel, anisotropic materials
Laser flash analysis (LFA) is the leading option for in-plane testing, but comes with drawbacks
  Expensive: DXF 200+ costs $130,000
  Not strictly in-plane

## Slide 3
Relies on the validity of the 1-D Heat Equation:
Setup
Thermocouple Readout
The Ångström Method
Our theoretical backbone

## Slide 4
Frame / Vacuum Chamber – How can we minimize convection?
Clamping – How can we reliably fixture our samples?
Heating / Electronics – How can we achieve controlled, sinusoidal heating?
Heat Sink – How can we maintain a constant temperature boundary condition?
Thermocouples – How can we achieve equal mechanical pressure?
Data Analysis – How can we most accurately output our data?
Subsystem Challenges
Notes: Vacuum is both a solution and a challenge

## Slide 5
CAD Model
CAD Model

## Slide 6
CAD Model
CAD Model – Design Iterations

## Slide 7: Sample Forces
  How will can we reliably fixture our sample?
  Total force exerted on sample on each side due to the weight of the block and a 23.2 lbs/in spring:
    Total Normal Stress exerted on sample contact area:
Clamping Forces

## Slide 8: Thermocouple Housing Selection
Performed test to measure consistency of applied pressure
  Both designs took >1 minute to settle on a value
  Sources of error for cantilever can be more easily accounted for
  Decision: Cantilever design
Thermocouple Housing
Notes: Another important aspect of our design is our thermocouple housing, which must maintain equal mechanical pressure for the 2 thermocouples placed along the sample. One proposed design was a spring-loaded mechanism where the turn of a screw by the user compresses a spring, thereby applying pressure to the thermocouple bead secured at the bottom. Another design was a much simper cantilever arm, which is secured about a shaft placed further back behind the sample. Equal pressure is achieved through the equal weight of each arm and, if needed, applying weights of known value on top of the arm.
We performed a test on 3D printed prototypes of both designs to quantify the consistency of the pressure applied. We found that both designs took over 1 minute to settle to a stable applied force, which is not ideal for a device where we want the user to reliably know at any point in time what the applied force is. We thought about what was causing this drift for each design and how we could improve upon it in future iterations. Ultimately, we decided on pursuing the cantilever design. Its drift is likely caused by lack of axial constraint along the shaft in our prints (as shown in this video). This can be easily designed for by using a bearing along the shaft in the final design. The spring-loaded mechanism, in contrast, has other, more complex factors that must be accounted for to ensure a constant, reliable force is achieved every time.

## Slide 9: Thermocouple Selection
Bead-type provides suitable geometry for measuring temperature at a single point
  More flexible than probe-type
  Not susceptible to self-heating like thermistors
Thermocouple Selection

## Slide 10
Chart: Cantilever Design
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120
Test 1 | 14.9 | 14.85 | 15.52 | 15.88 | 16.23 | 16.59 | 16.47 | 16.65 | 16.66 | 16.75 | 16.78 | 16.76 | 16.71
Test 2 | 15.27 | 15.26 | 15.46 | 15.67 | 15.72 | 15.74 | 15.69 | 15.75 | 15.85 | 15.83 | 15.88 | 15.82 | 15.74
Notes: Value takes time to settle, and not consistent between identical tests
11/29 Test: both TC’s stayed at 14-15g for at least 1 minute

## Slide 11
Chart: Spring-Loaded Design
| 0 | 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120
Smaller Turn | 33.78 | 31.78 | 30.63 | 29.89 | 29.4 | 28.99 | 28.58 | 28.31 | 28.18
Larger Turn | 31.15 | 30.84 | 30.63 | 30.55 | 30.42 | 30.3 | 30.12 | 29.92 | 29.7 | 29.58 | 29.56 | 29.43 | 29.28 | 29.33 | 29.27 | 29.22 | 29.22 | 29.17 | 29.18 | 29.13 | 29.07

## Slide 12
Ansys Simulations – Simple

## Slide 13
Ansys Simulations - Refined

## Slide 14
Ansys Simulations – Sine Wave

## Slide 15
Ansys Simulations - Heatsink

## Slide 16: Data Collection
DAQ Buffer Size | 15 Values
X Time Between Readings | 0.3 Seconds
Storage Time on DAQ Buffer | 4.5 Seconds
Should take a reading every 4.5 seconds to ensure data is not lost
Data Processing must be Fast
How can we ensure all data is collected?

## Slide 17: Data Collection
Current Data Processing takes ~0.6 seconds
Limited to a 4.5 second window to ensure data is not lost
Will ensure speed as features increase (Heater control, more TC, etc.)

## Slide 18: Electrical Simulation
Get an understanding of the switching behavior of our MOSFETs
Guide PCB Design

## Slide 19: PCB Design
Simple soldering
Reduce risk of errors/shorts

## Slide 20: Thank You!
Any Questions?